Self-Driving Car using Convolutional Neural Network
Chris Winsor
9/1/2018

The experiment applies a Convolutional Neural Network (CNN) to the task of making a self-driving car. The car is taught to follow a track which defined as a piece of orange tape on a white carpet floor. Data consists of left/right control signals of an operator as the car is driven and images from a forward-mounted camera. The CNN is trained to predict left/right control signal from the camera image. The CNN is then used to control the car without user input. The project demonstrates the use of a CNN in a real-world application.

The software library is Python/Scikit-Learn/TensorFlow. The hardware platform is Raspberry Pi/Raspbian.

This document includes:
- Overview of the car, track and general approach
- Hardware: interfacing the RaspberryPi to the RC controller and Pi Camera
- Software: CNN architecture, database structure, files, and approach to data collection

# References and Links

Source Code and Processed (categorical) Data:
https://github.com/cwinsor/metrowest_scikit_tensorflow_cnn_car

Metrowest Boston Developers Machine Learning Group:
1. Meetup: Metrowest Boston Developers Machine Learning Group
2. Github: https://github.com/geneostrat/Metrowest-Developers-Machine-Learning-Group
3. Raw data (proportional control): https://github.com/geneostrat/TrainingData.git

Hands-On Machine Learning with Scikit-Learn & TensorFlow, Geron, O'Reilly, First Edition
<reference to the 2 datasets, and to the examples>

# Overview
The Car
The car was the “RC Trucks” by New Bright ($10 Walmart). It includes a Handheld Controller with forward/backward and left/right (non-proportional) controls. The communication link between controller and car is 49mhz.

The Track
The car was taught to follow a “track” which is a piece of orange tape on a white carpet floor. We chose the Oval shape although there are several interesting options including Dog-bone and Figure 8.

The Raspberry Pi
For on-board processing we used a Raspberry PI 2 Model B with optional Camera running the Raspbian (Ubuntu Linux).

Software
The CNN wascreated using Google's Scikit/Tensorflow library and computation framework. Training of the CNN was done on google cloud. There are two small python applications for the on-board Pi. The first is used to capture data, and the second applies the trained CNN to drive the car. We use the standard Raspibian Linux on the Raspberry PI with the (????) library.

General Approach
In the “Data Capture” phase directional control signals and images from the camera were captured as a user drove the car. This data was then copied to a cloud compute farm where the Scikit/TensorFlow library was used to train a Convolutional Neural Network (“CNN”). The output of training was set of parameter weights for the CNN. The CNN was later in-instanced on the Pi and parameter weights applied. ThePi was then able to use the CNN to convert realtime image from the camera to generate left/right control signals to drive the car.

Some tactical considerations:
During training the Pi needs to be two places at the same time - on the car taking pictures, and near the Handheld Controller observing signals into the DK2970. To solve this we will use a cable so the Pi can be on the car, but can observe the signals going into the DK2970. There is no problem during Runtime since the Handheld Controller can be relocated to the car (no user is required) so it is co-resident with the Pi.

Hacking the Handheld Controller
Inside the controller is a small circuit board with four button switches (left/right/forward/reverse), a transmitter chip (DK2970), and analog components to support the antenna. The chip handles everything - taking in the 4 control signals and outputting the 49mnz carrier. The control signal inputs are 2.1 volt “open drain” - a push of the button grounds the signal. The pullup is internal to the chip and measured at 660kohm. We are fortunate in that signal levels are compatible with the Pi GPIO.

During training the Pi wants to receive the left/right signals. During runtime the Pi will be driving them. The brute force approach (shown in the “Architecture Diagram”) involves breaking the signal between the button and the DK2970, having the Pi intercept, observe, and output the signals during training. In theory this is the correct approach, it would require 2 wires (a 'receive' and transmit') to/from the Pi for Left and 2 for Right (4 total).
A simpler approach can be pursued given the open-drain signal of this controller. During training the Pi simply observes the Handheld Controller signals - the push buttons on the Handheld Controller ground the wire to produce the signal. During runtime the handheld still provides the pullup, but the Pi will ground the wire to produce the signal. This means only 1 wire is needed between Handheld Controller and Pi for each of Left and Right (2 total).

Noise is a consideration especially considering the weak 660Kohm pullup and the length of the cable. We used CAT5 twisted pair to reduce noise exposure.
Finally - we added a CAT5 connector - this allows substituting a shorter cable during Runtime when the Handheld Controller will be riding on the car near the Pi.

GPIO connector and Software
For physical wiring we chose GPIOs 26 and 16 and again used a CAT5 connector. A reference for GPIO pinning on the Pi2-B (that is actually *correct*) is https://www.youtube.com/watch?v=6PuK9fh3aL8

Code to verify signaling between Pi GPIO and Handheld Controller is in Appendix X.
We use the “gpiozero' python library https://gpiozero.readthedocs.io/en/stable/index.html .

With the above wiring and software we are able to demonstrate the Pi can capture the necessary signal and camera training data, and can drive the left/right signals to turn the car. Now it is time to capture data!

Capturing Data
The Pi is zip-tied to the top of the car. A USB battery provides power for the Pi. The camera is rubber-banded to the front grill. The CAT5 provides the control signals to the Pi for observation during training.

We laid out an “Oval” track. We ran the car around the track in clockwise and counter-clockwise directions - a total of 11 loops. Each loop is about a minute and the capture rate is 2/second.

Raw data and Python code as is available on the Github.

The Dataset

The dataset is a collection of images and steering from a toy car as it is driven around a track.

The track is set up on a concrete floor. A piece of tape defines the centerline and the car will be trained to follow this line. During training the steering values applied by the driver to keep the car on the track are captured.

The dataset is split into training and test subsets of size 2582 and 646 respectively.

Images are square, size 64x64 using RGB encoding. This is kept as a 4-dimensional numpy array of numpy.uint8. The dimensions of this array are [N][64][64][3]. The first dimension is image number. The next two dimensions are height, width. The final dimension is color.

Steering values are categorical with 1=left, 3=straight 2=right. The data is kept as a 1-dimensional numpy array of numpy.uint8. The array is size [N] which is the direction the car is being steered at the time of the correspondingly-numbered image.

The structure of the dataset is:

- "DESCR" - an overview description of the dataset.
- "images_train" - training images
- "images_test" - testing image
- "steering_train" - training steering values
- "steering_test" - testing steering values
- "target_names" - a list of values of the steering class [1, 3, 2]

Appendix 1:
The following code was used when hacking the Handheld Contrlller and Pi to demonstrate operation of the physical wiring and connections between Handheld Controller and Pi GPIO via the CAT5 cable. This is a subset of the full code which is available on github.

The “train” switch sets the mode of operation. In “train” mode the Pi observes GPIOs and prints a left/right message when the Handheld Controller left/right buttons are pushed. In “non-train” (driving) mode the Pi will output left and right signals on a 1 second period. If the car is powered the front wheels will follow the Handheld Controller (training) or the Pi (driving). Camera images are also captured in “train” mode.

from gpiozero import InputDevice
from gpiozero import OutputDevice
from picamera import PiCamera
from time import sleep

train = True

pin_left = 26
pin_right = 13

if train == True:

        pin_l = InputDevice(pin_left,True)
        pin_r = InputDevice(pin_right,True)

        camera = PiCamera()
        camera.start_preview()
        sleep(5)
        i = 0
        while True:
        if pin_l.value:
        print("Left")
        if pin_r.value:
pi@raspberrypi2:~/tempdir$ more temp.py
from gpiozero import InputDevice
from gpiozero import OutputDevice
from picamera import PiCamera
from time import sleep

train = True

pin_left = 26
pin_right = 13

if train == True:

        pin_l = InputDevice(pin_left,True)
        pin_r = InputDevice(pin_right,True)

        camera = PiCamera()
        camera.start_preview()
        sleep(5)
        i = 0
        while True:
        if pin_l.value:
        print("Left")
        if pin_r.value:
        print("Right")

        camera.capture('/home/pi/tempdir/pictures/image%s.jpg' % i)
        i = i + 1
        sleep(1)
        camera.stop_preview()

if train == False:

        pin_l = OutputDevice(pin_left,True,True)
        pin_r = OutputDevice(pin_right,True,True)

        while True:
        print("center")
        pin_l.on()
        pin_r.on()
        sleep(1)

        print("right")
        pin_l.on()
        pin_r.off()
        sleep(1)

        print("center")
        pin_l.on()
        pin_r.on()
        sleep(1)

        print("left")
        pin_l.off()
        pin_r.on()
        sleep(1)